## Slide 1
Etienne Parizot
(APC – Université Paris Diderot - France)
Observation of ultra-high-energy cosmic rays from space
JEM-EUSO and pathfinders
ONR-APC-IPGP meeting — 29th October 2014

## Slide 2
100 MeV
1021 eV
~ 1 particle/m2/second
Energy
Flux
~ 1 particle/m2/year
~ 1 particle/m2/billion year!
The cosmic ray energy spectrum
Ultra-high-energy cosmic rays (UHECRs)

## Slide 3: How JEM-EUSO works
“extensive air shower”
Detect UHECR-induced showers through the fluorescence light generated in the atmosphere
UV fluorescence spectrum
~100 billion particles!
1 cosmic ray

## Slide 4: JEM-EUSO and its pathfinders…
EUSO-TA (telescope array)
JEM-EUSO
Mini-EUSO
EUSO-Balloon
(+ KLYPVE-EUSO)

## Slide 5: Focal surface
137 PDM of 9 EC, each EC has 4 PMT with 64 pixels each
4932 PMT and 0.3156 Megapixels
PDM

## Slide 6
Photo-Detection Module (PDM)

## Slide 7: Characteristics and advantages
Huge field of view (60° aperture)
Ultra-sensitive UV camera (single photon counting)
Ultra-fast camera (2.5 µs  400 000 images/second)
Over 300 000 pixels
Full-sky coverage, over several years
+ infrared camera + LIDAR
Large dynamic range (automatic gain switches)

## Slide 8: Many possible synergies
Atmospheric sciences
Cloud coverage
TLEs (sprites, jets, elves, halos…)
Sciences of the ocean
Can a surface water temperature survey (3K accuracy) be useful?
Surface bioluminescence
Links between cosmic rays and lightning
Meteorites sciences
Others?
Statistics, Trajectories, Recovery…
LIDAR reflection  water level?
Space debris removal
identification, trajectory  laser shot
Airglow (nightglow) monitoring
Plant fluorescence…

## Slide 9: EUSO-Balloon
Pathfinder to JEM-EUSO (CNES mission)
Successful flight on August 24th, 2014 (Timmins, Ontario)

## Slide 10: EUSO-Balloon
Pathfinder to JEM-EUSO (CNES mission)
Data on the UV background and its space/time variability
Technology demonstration
Observation of artificial transient events
laser shots + LED + Xenon flashers (US/NASA)
• additional to the airglow
• investigation of different types of ground / albedos

## Slide 11: EUSO-Balloon + helicopter

## Slide 12: EUSO-Balloon
The data are being analyzed right now!

## Slide 13: EUSO-Balloon

## Slide 14: EUSO-Balloon

## Slide 15: EUSO-Balloon

## Slide 16: EUSO-Balloon

## Slide 17: EUSO-Balloon

## Slide 18: EUSO-Balloon

## Slide 19: EUSO-Balloon

## Slide 20: EUSO-Balloon

## Slide 21: EUSO-Balloon

## Slide 22: EUSO-Balloon

## Slide 23: EUSO-Balloon

## Slide 24: Space debris removal
Strategy
JEM-EUSO can detect and determine the trajectory of debris in the critical 1 cm – 10 cm range!

## Slide 25: Next steps
Approved mission
JEM-EUSO demonstrator onboard the ISS (inside, not outside)
ASI (Italian Space Agency) and ROSCOSMOS)
Will observe airglow from space
Will observe TLEs and meteors
Can demonstrate space debris removal strategy
Will include test SiPMT detectors
(to be operated in the ISS in 2017)
Long duration balloon flight
Expected strong support from both CNES and NASA
Key milestone: detect the first UHECR showers from above (with the fluorescence technique, well established on ground)
Mini-EUSO

## Slide 26: Thank you!

## Slide 27: Back-up slides
Transient luminous events
Meteor(ite)s
EUSO-Balloon
Space debris removal strategy

## Slide 28
Back up - I – Transient luminous events (TLEs)

## Slide 29
TLEs (sprites, jets, elves, halos …) are the effects of intensive interaction between different regions in the space around Earth

## Slide 30: Ionosphere phenomena

## Slide 31
TLE are associated with the electromagnetic connections and interactions between atmosphere, ionosphere and magnetosphere and with strong thunderstorm activity

## Slide 36
Subtle structure of the sprite

## Slide 39
Blue and giant blue jets

## Slide 41: Blue Jet structure [Wescott,et al., JGR, 2001]
At the base of the jet the diameter ~400m.
The diameter does not vary till ~22 km.
At 27 km it broadens to ~2 km, and is ~3 km at 35 km.
Eight smaller streamers with 50-100 m diameter detected.
Lifetime of the event ~0.1 s.
Was not associated with any particular CG lightning.
The total optical brightness reached 6.7 MR (0.5 MJ of optical energy).
0.4km
2km
3km
50-100m

## Slide 43
RHESSI : (Terrestrial Gamma Flashes TGFs)
Smith et al., 2005
498 events in 37 months

## Slide 45
Interaction with radiation belt

## Slide 46
2009 TOHOKU UNIVERSITY

## Slide 47
Tool for the Analysis of RAdiations
from lightNIngs and Sprites =TARANIS

## Slide 48: THE ATMOSPHERIC-SPACE INTERACTION MONITOR

## Slide 50
FILAMENTATION OF THE SPACE PLASMA

## Slide 53: Field-Aligned Currents and Filaments in Space Plasmas
Filamentary strucures are found in the following space plasmas, all of which are observed or are likely to be associated with electric currents:
1.In the aurora filaments parallel to the magnetic field are often observed. These can have dimensions down to 100m.
2. Inverted V events (105 -106 A) and in situ measurements of the electric currents in the magnetosphere demonstrate the existence of the filamentary structures
3. In the ionosphere of Venus „flux ropes” or „magnetic ropes”, whose filamentary diameter are typically 20km, are observed.

## Slide 54
4.In the Sun, prominences (1011A), spicules, coronal streamers, polar plumes etc. Show filamentary structure whose dimensions are in order 107-108m.
5.The cometary tails often have a pronounced filamentary structure.
6.In the interstelar medium and in the interstelar clouds there is a abundance of the filamentary structures.
7.The center of the Galaxy, where twisting plasma filaments, apparently held together by magnetic field possesing both azimutal and poloidal components, extend for nearly 60pc (1018 m.)

## Slide 55: Physical Mechanisms of Filamentation
There are two fundamental physical mechanisms trying to explain a creation of the filamentary structure in the space plasmas. Both are associated with currents and ambient magnetic field.
1.Pinch instability of the field aligned electric current (Galperin et al. 1986)
2.Filament instability of the dispersive Alfven waves (Shukla and Stenflo 1989, Lavader et al. 2001)

## Slide 57
SUMMARY
The characteristics of the TLE’s have been described by different groups working with detectors on the orbit and on ground detecting systems.
JEM EUSO is unique in that its time and spatial resolution is very high and it will allow to see evolution in time of the subtle structure (filamentation) of TLE’s.
There will be two more experiments dedicated to measuring the TLEs on the orbit soon ASIM and Taranis.
The set of data produced by all these experiments may create an exceptional chance to further investigate the physical nature of the TLEs.

## Slide 58
Back up - II - Observation of meteor(ite)s with JEM-EUSO

## Slide 68
Back up – III – EUSO-Balloon

## Slide 69: EUSO-BALLOON
A balloon-borne fluorescence telescope, pathfinder of JEM-EUSO
1 PDM with electronics and mechanics as close as possible to JEM-EUSO
DAQ & BG study
Detection EAS > ~1018eV from an altitude of 40km (expected 0.2-0.3 events with E>2×1018 eV during 10 hours night-flight)
CNES project with IRAP, APC & LAL + support of the whole JEM-EUSO collaboration
 | JEM-EUSO | EUSO-BALLOON
Height [km] | 420 | 40
Diameter [m] | 2.5 | 1
FoV/pixel [deg] | 0.08 | 0.25
Pixel@ground [km] | 0.058 | 0.175
FoV/PDM [deg] | 3.8 | 12(8)
PDM@ground [km] | 28.2 | 8.4
Signal Ratio | 1 | 17.6
BG Ratio | 1 | 0.9-1.8
S/√N | 1 | 20-10
Eth [eV] | 3×1019 | 1.5-3×1018
# of PDM | 137 | 1
1st launch was successfully carried out on August 24-25th 2014, Timmins (Canada)

## Slide 70
Balloon
EUSO
detector
4 km
~40 km
Calibrated
Flash lamp
Testing EUSO-Balloon
Fly one aircraft equipped with
two types of calibrated pulsed UV light sources.
Point Test: Fly airplane in field of view and fire flash lamp. Light travels directly from lamp to detector
Track Test: Fly airplane outside field of view and shoot a UV pulsed laser across field of view. Light scatters out of the beam to the detector.
(5 mJ Laser ~100 EeV Cosmic Ray)
Fly aircraft at altitudes between 1-5 km.
Field of View
Point
Test
Helicopter equiped with
laser and Xenon flasher
EUSO-BALLOON ‘‘in flight’’ calibration

## Slide 71: EUSO-BALLOON Instrument
Instrument
• Mechanical structure (gondola)
• Optics: 2 flat Fresnel lenses (L1&L3)
• 1 Photodetector Module (PDM)
• Data acquisition system (DAQ)
• Monitoring controlled by House Keeping system (HK)
• A set of power supplies (LVPS) powered by onboard batteries (Power Pack)
• An IR camera for atmospheric monitoring

## Slide 72: EUSO-BALLOON Data Acquisition (DAQ) Chain
Front-end (FE) electronics
PMT
• Hmamatsu 64-ch MAPMT
• BG3 filter
EC-Unit
• 4 PMTs (256-ch)
readout cables
• HV board
• potting
Sensor (photodetector)
EC-ASIC
• 6 x ASICs
• readout
• counter
PDM-Board
• Slow control
• Level 1 (L1, track) trigger
CPU
• Run control, config. FE electronics
• Console & GUI, remote access, etc.
• Data processing
• managing Mass Memory for data
storage
CCB
(Cluster Control Board)
• Receive data
from 9 PDMs
Data Processing (DP)
HK, LVPS
IR camera

## Slide 73: EUSO-Balloon

## Slide 74: CNES Flight Chain
valve
covering
Discharge sleeve
Remote separator
Parachute tension
Operational servitude pod (NSO)
Radar refector
Beacon
Alticoder radar
responder
dampers
(EUSO-BALLOON main frame)
Scirnetific equipment
Scirnce telemetry pod
Main elements
of an open
Stratospheric
balloon
100 m
~ 150 m
20 m
~ 180 m

## Slide 75: Laser track
Event profile

## Slide 76: Other instruments onboard
Infrared Camera (IR Camera)
NIST photodiode
Gerger counter
GPS
Attitude sensor
GoPro camera
Independent of data acquisition systems
Offline synchronization (UTC time stamps)

## Slide 77: Complementary and/or anecdotal data
  Light intensity (NIST)
  Temperature eveolution
  Cosmic ray intensity (Geiger)
  Infrared data

## Slide 78
Back up – IV – Space debris removal strategy

## Slide 79
Quinn et al. (2014): Acta Astronautica 105, 192-200

## Slide 80
Quinn et al. (2014): Acta Astronautica 105, 192-200

## Slide 81
Quinn et al. (2014): Acta Astronautica 105, 192-200