## Slide 1
Etienne Parizot
(APC – Université Paris Diderot - France)
Observation of ultra-high-energy cosmic rays from space
JEM-EUSO and pathfinders
ONR-APC-IPGP meeting — 29th October 2014

## Slide 2
100 MeV
1021 eV
~ 1 particle/m2/second
Energy
Flux
~ 1 particle/m2/year
~ 1 particle/m2/billion year!
The cosmic ray energy spectrum
Ultra-high-energy cosmic rays (UHECRs)

## Slide 3: How JEM-EUSO works
“extensive air shower”
Detect UHECR-induced showers through the fluorescence light generated in the atmosphere
UV fluorescence spectrum
~100 billion particles!
1 cosmic ray

## Slide 4: JEM-EUSO and its pathfinders…
EUSO-TA (telescope array)
JEM-EUSO
Mini-EUSO
EUSO-Balloon
(+ KLYPVE-EUSO)

## Slide 5: Focal surface
137 PDM of 9 EC, each EC has 4 PMT with 64 pixels each
4932 PMT and 0.3156 Megapixels
PDM

## Slide 6
Photo-Detection Module (PDM)

## Slide 7: Characteristics and advantages
Huge field of view (60° aperture)
Ultra-sensitive UV camera (single photon counting)
Ultra-fast camera (2.5 µs  400 000 images/second)
Over 300 000 pixels
Full-sky coverage, over several years
+ infrared camera + LIDAR
Large dynamic range (automatic gain switches)

## Slide 8: Many possible synergies
Atmospheric sciences
Cloud coverage
TLEs (sprites, jets, elves, halos…)
Sciences of the ocean
Can a surface water temperature survey (3K accuracy) be useful?
Surface bioluminescence
Links between cosmic rays and lightning
Meteorites sciences
Others?
Statistics, Trajectories, Recovery…
LIDAR reflection  water level?
Space debris removal
identification, trajectory  laser shot
Airglow (nightglow) monitoring
Plant fluorescence…

## Slide 9: EUSO-Balloon
Pathfinder to JEM-EUSO (CNES mission)
Successful flight on August 24th, 2014 (Timmins, Ontario)

## Slide 10: EUSO-Balloon
Pathfinder to JEM-EUSO (CNES mission)
Data on the UV background and its space/time variability
Technology demonstration
Observation of artificial transient events
laser shots + LED + Xenon flashers (US/NASA)
• additional to the airglow
• investigation of different types of ground / albedos

## Slide 11: EUSO-Balloon + helicopter

## Slide 12: EUSO-Balloon
The data are being analyzed right now!

## Slide 13: EUSO-Balloon

## Slide 14: EUSO-Balloon

## Slide 15: EUSO-Balloon

## Slide 16: EUSO-Balloon

## Slide 17: EUSO-Balloon

## Slide 18: EUSO-Balloon

## Slide 19: EUSO-Balloon

## Slide 20: EUSO-Balloon

## Slide 21: EUSO-Balloon

## Slide 22: EUSO-Balloon

## Slide 23: EUSO-Balloon

## Slide 24: Space debris removal
Strategy
JEM-EUSO can detect and determine the trajectory of debris in the critical 1 cm – 10 cm range!

## Slide 25: Next steps
Approved mission
JEM-EUSO demonstrator onboard the ISS (inside, not outside)
ASI (Italian Space Agency) and ROSCOSMOS)
Will observe airglow from space
Will observe TLEs and meteors
Can demonstrate space debris removal strategy
Will include test SiPMT detectors
(to be operated in the ISS in 2017)
Long duration balloon flight
Expected strong support from both CNES and NASA
Key milestone: detect the first UHECR showers from above (with the fluorescence technique, well established on ground)
Mini-EUSO

## Slide 26: Thank you!